## Slide 1
SKYGUARD AI
Weather station
integrity monitor
Detect sensor faults. Classify the signal. Recover a trusted current reading.
24
HOUR TELEMETRY WINDOW
Temperature • Pressure • Humidity
Project summary and presentation guide
Notes: Opening: “Our project is SkyGuard, a weather station integrity monitor. It analyzes a day of hourly temperature, pressure, and humidity data, flags suspicious sensor behavior, and returns smoothed readings for the current hour. I’ll walk through what we built and who it is intended to help.”

## Slide 2
SKYGUARD PROJECT WALKTHROUGH
The problem: unreliable station readings
SKYGUARD AI • PROJECT OVERVIEW
•
A stuck, drifting, or spiking sensor can make a station feed misleading.
•
A sudden real weather change can look like a sensor fault.
•
Operators need a clear alert and a usable current reading.
INPUT
Hourly station telemetry
Temperature · Pressure
Relative humidity · Hour
OUTPUT
Health status + recovered values
Notes: “The problem we focused on is data quality. A sensor can flatline, drift, or jump unexpectedly. At the same time, genuine severe weather can produce abrupt changes, so an anomaly detector has to interpret context and communicate its result.”

## Slide 3
SKYGUARD PROJECT WALKTHROUGH
What we built
SKYGUARD AI • PROJECT OVERVIEW
01
Load data
24 chronological readings
→
02
Detect
LSTM reconstruction + signal checks
→
03
Interpret
Fault category or severe-weather pass
→
04
Recover
Kalman-smoothed current values
Browser dashboard → FastAPI diagnosis endpoint → results
Notes: “The full path starts in the dashboard, where a user loads or edits 24 hourly readings. The browser sends them to the FastAPI service. The service combines the trained model with checks for suspicious signal patterns, then returns a status, fault type, and observed versus healed values.”

## Slide 4
SKYGUARD PROJECT WALKTHROUGH
Detection and recovery
SKYGUARD AI • PROJECT OVERVIEW
DETECTION
•
LSTM autoencoder reconstructs the telemetry sequence.
•
Reconstruction error is compared with a configured threshold.
•
Rules check flatlines, pressure jumps, and storm-like changes.
RECOVERY
•
Kalman filters process temperature, pressure, and humidity.
•
Prior readings warm up each filter.
•
When current data is flagged, the estimate is held instead of accepting it.
Configured reconstruction threshold: 0.037624
Notes: “Detection has two parts. The LSTM autoencoder measures how unusual the latest physical readings look relative to the learned sequence. Additional checks catch flatlined humidity or temperature and sudden pressure jumps. A pressure drop paired with a humidity rise can be treated as a severe-weather pass. For recovery, a separate one-dimensional Kalman filter per variable smooths the signal and skips a flagged current measurement.”

## Slide 5
SKYGUARD PROJECT WALKTHROUGH
Dashboard and service
SKYGUARD AI • PROJECT OVERVIEW
THE WEB DASHBOARD
•
Shows service/model readiness and diagnosis results.
•
Loads sample values or hourly Open-Meteo estimates.
•
Displays alert, fault type, error, threshold, and readings.
THE API
•
GET /health reports service and artifact status.
•
POST /api/v1/diagnose accepts exactly 24 readings.
•
GET /docs provides interactive API documentation.
Location search and weather refresh use Open-Meteo; internet required.
Notes: “The website is the operational interface for the demo. It checks whether the backend and model artifacts are loaded, accepts sample data or a selected location, and visualizes the result. Developers can also call the API directly or use FastAPI’s interactive docs. Live weather is sourced from Open-Meteo estimates.”

## Slide 6
SKYGUARD PROJECT WALKTHROUGH
Tools and technology
SKYGUARD AI • PROJECT OVERVIEW
Python 3.12
Runtime for the service and model
FastAPI + Uvicorn
HTTP API, validation, docs, local web serving
PyTorch
LSTM autoencoder inference
NumPy + scikit-learn
Feature arrays and robust scaling
Joblib
Loads the saved scaler
HTML / CSS / JavaScript
Browser dashboard and API calls
Open-Meteo APIs
Geocoding and hourly weather estimates
Notes: “The stack is deliberately straightforward. Python and FastAPI serve the inference endpoint; PyTorch runs the LSTM model; NumPy and scikit-learn prepare and scale features; Joblib loads the saved scaler. The front end is plain HTML, CSS, and JavaScript. Open-Meteo supplies city lookup and hourly weather estimates.”

## Slide 7
SKYGUARD PROJECT WALKTHROUGH
Who the site is for
SKYGUARD AI • PROJECT OVERVIEW
PRIMARY USERS
•
Weather station operators checking incoming telemetry.
•
Developers integrating or evaluating sensor-quality APIs.
•
Hackathon judges and teams demonstrating anomaly detection.
USE IT TO
Review a 24-hour window
Spot likely sensor faults
See the current reading after smoothing
Prototype / demonstration scope
Notes: “The intended audience is people responsible for weather telemetry and the developers building around those feeds. It is also designed to be understandable in a hackathon demo. The repository positions this as a demonstration and development service, not a deployed production monitoring system.”

## Slide 8
SKYGUARD PROJECT WALKTHROUGH
Data source and demo limits
SKYGUARD AI • PROJECT OVERVIEW
•
Open-Meteo returns model-based weather estimates for a selected location.
•
Those values are not readings from a physical AWS sensor.
•
Sample data supports an offline demonstration.
•
Python 3.12 and the saved model/scaler artifacts are needed to run the service.
Describe anomaly results as a demonstration of the SkyGuard model.
Notes: “One important limitation: the live-weather mode fetches model-based estimates from Open-Meteo; it does not connect to an AWS physical sensor. We can demonstrate the diagnosis with synthetic sample readings even without internet access. The project documentation recommends Python 3.12 and requires the model and scaler files.”

## Slide 9
SKYGUARD PROJECT WALKTHROUGH
Demo flow and close
SKYGUARD AI • PROJECT OVERVIEW
1
Start API
uvicorn main:app
2
Open dashboard
localhost:8000
3
Choose data
Sample or city search
4
Run diagnosis
Review alert + healed values
SkyGuard turns a day of weather telemetry into an explainable health check.
Notes: “To demo it, start the API, open the dashboard, load sample data or search for a city, and run diagnostics. Then explain the status, fault category, reconstruction error, and observed versus healed values. SkyGuard is a prototype for making weather telemetry easier to inspect and recover.”